## Slide 1: 11. Input-Output Organization
11-1 Peripheral Devices
  I/O Subsystem
    Provides an efficient mode of communication between the central system and the outside environment
  Peripheral (or I/O Device)
    Input or Output devices attached to the computer
      Monitor (Visual Output Device) : CRT, LCD
      KBD (Input Device) : light pen, mouse, touch screen, joy stick, digitizer
      Printer (Hard Copy Device) : Dot matrix (impact), thermal, ink jet, laser (non-impact)
      Storage Device : Magnetic tape, magnetic disk, optical disk
  ASCII (American Standard Code for Information Interchange) Alphanumeric Characters
    I/O communications are usually involved in the transfer of ASCII information
    ASCII Code : Tab. 11-1
      7 bit : 00 - 7F ( 0 - 127 )
        80 - FF ( 128 - 255 )
11-2 Input-Output Interface
  Interface
    1) A conversion of signal values may be required

## Slide 2
    2) A synchronization mechanism may be needed
      The data transfer rate of peripherals is usually slower than the transfer rate of the CPU
    3) Data codes and formats in peripherals differ from the word format in the CPU and Memory
    4) The operating modes of peripherals are different from each other
      Each peripherals must be controlled so as not to disturb the operation of other peripherals connected to the CPU
  Interface
    Special hardware components between the CPU and peripherals
    Supervise and Synchronize all input and output transfers
  I/O Bus and Interface Modules : Fig. 11-1
    I/O Bus
      Data lines
      Address lines
      Control lines
    Interface Modules :
      SCSI (Small Computer System Interface)
      IDE (Integrated Device Electronics)
      Centronics
      RS-232
      IEEE-488 (GPIB)

## Slide 3
    I/O command : 8251 SIO 예제
      Control Command
      Status Command
      Input Command
      Output Command
  I/O Bus versus Memory Bus
    Computer buses can be used to communicate with memory and I/O
      1) Use two separate buses, one for memory and the other for I/O : Fig. 11-19, p. 421
        I/O Processor
      2) Use one common bus for both memory and I/O but have separate control lines for each : Isolated I/O or I/O Mapped I/O
        IN, OUT : I/O Instruction
        MOV or LD : Memory read/write Instruction
      3) Use one common bus for memory and I/O with common control lines : Memory Mapped I/O
        MOV or LD : I/O and Memory read/write Instruction
Intel, Zilog
Motorola
* Control Lines
I/O Request, Mem Request, Read/Write
* Control Lines
Read/Write

## Slide 4
  Example of I/O Interface : Fig. 11-2
    4 I/O port : Data port A, Data port B, Control, Status
      8255 PIO ( port A, B, C, Control/Status )
    Address Decode : CS, RS1, RS0
11-3 Asynchronous Data Transfer
  Synchronous Data Transfer
    All data transfers occur simultaneously during the occurrence of a clock pulse
    Registers in the interface share a common clock with CPU registers
  Asynchronous Data Transfer
    Internal timing in each unit (CPU and Interface) is independent
    Each unit uses its own private clock for internal registers

## Slide 5
  Strobe : Control signal to indicate the time at which data is being transmitted
    1) Source-initiated strobe : Fig. 11-3
    2) Destination-initiated strobe : Fig. 11-4
    Disadvantage of strobe method
      Destination 이 Data
      Handshake method
Fig. 11-3 Source-initiated strobe
Fig. 11-4 Destination-initiated strobe





## Slide 6
  Handshake : Agreement between two independent units
    1) Source-initiated handshake : Fig. 11-5
    2) Destination-initiated handshake : Fig. 11-6
    Timeout : If the return handshake signal does not respond within a given time period, the unit assumes that an error has occurred.
Fig. 11-5 Source-initiated handshake
Fig. 11-6 Destination-initiated handshake







## Slide 7
  Asynchronous Serial Transfer
    Synchronous transmission : Sec. 11-8
      The two unit share a common clock frequency
      Bits are transmitted continuously at the rate dictated by the clock pulses
    Asynchronous transmission : Fig. 11-7
      Special bits are inserted at both ends of the character code
      Each character consists of three parts :
        1) start bit : always “0”, indicate the beginning of a character
        2) character bits : data
        3) stop bit : always “1”
    Asynchronous transmission rules :
       When a character is not being sent, the line is kept in the 1-state
       The initiation of a character transmission is detected from the start bit, which is always “0”
       The character bits always follow the start bit
       After the last bit of the character is transmitted, a stop bit is detected when the line returns to the 1-state for at least one bit time





## Slide 8
    Baud Rate : Data transfer rate in bits per second
      10 character per second with 11 bit format = 110 bit per second
    UART (Universal Asynchronous Receiver Transmitter) : 8250
    UART (Universal Synchronous/Asynchronous Receiver Transmitter) : 8251
  Asynchronous Communication Interface : Fig. 11-8
    8250 SIO
      80 : Data Write/Read (Transmit/Receive)
      81 : Control Write/ Status Read
        A0 = RS (register select)
    Double Buffered (in transmit register)
      New character can be loaded as soon as
      the previous one starts transmission
    3 possible errors (in status register)
      1) parity error
        Even or Odd parity error
      2) framing error
        right number of stop bits is not detected
        at the end of the received character
      3) overrun error
        CPU does not read the character from
        the receiver register before the next one is available

## Slide 9
  First-In, First-Out (FIFO) Buffer : Fig. 11-9
    Fi : F4 = 1 = Output ready
      1 = valid data in Ri
      0 = no valid data in Ri
    Fi’ : F1’ = 1 = Input ready
      1 = empty in Ri
      0 = full in Ri
    Data Input
      1) Input ready = 1 (F1’ = 1)
      Insert = 1
      2) AND gate
      3) S = 1
      F1 = 1
      4) R2 F2’ = 1 이고
      F1 = 1 과 AND gate
      R1
    Data Output
      1) Output ready = 1 (F4 = 1= 1 로 하여 데이터 출력
      2) Delete = 1
      3) Delete
F1 = 0
F1’ = 1
S = 0

## Slide 10
11-4 Modes of Transfer
  Data transfer to and from peripherals
    1) Programmed I/O : in this section
    2) Interrupt-initiated I/O : in this section and sec. 11-5
    3) Direct Memory Access (DMA) : sec. 11-6
    4) I/O Processor (IOP) : sec. 11-7
  Example of Programmed I/O : Fig. 11-10, 11-11
  Interrupt-initiated I/O
    1) Non-vectored : fixed branch address
    2) Vectored : interrupt source supplies the branch address (interrupt vector)

## Slide 11
  Software Considerations
    I/O routines
      software routines for controlling peripherals and for transfer of data between the processor and peripherals
    I/O routines for standard peripherals are provided by the manufacturer (Device driver, OS or BIOS)
    I/O routines are usually included within the operating system
    I/O routines are usually available as operating system procedures ( OS or BIOS function call)
11-5 Priority Interrupt
  Priority Interrupt
    Identify the source of the interrupt when several sources will request service simultaneously
    Determine which condition is to be serviced first when two or more requests arrive simultaneously
    처리 방법 :
      1) Software : Polling
      2) Hardware : Daisy chain, Parallel priority

## Slide 12
  Polling
    Identify the highest-priority source by software means
      One common branch address is used for all interrupts
      Program polls the interrupt sources in sequence
      The highest-priority source is tested first
    Polling priority interrupt
      If there are many interrupt sources, the time required to poll them can exceed the time available to service the I/O device
      Hardware priority interrupt
  Daisy-Chaining : Fig. 11-12
“1”
“1”
“0”
Device 2
Interrupt Request

## Slide 13
    One stage of the daisy-chain priority arrangement : Fig. 11-13
     No interrupt request
     Invalid : interrupt request, but no acknowledge
     No interrupt request : Pass to other device (other device requested interrupt )
     Interrupt request




INTACK
INT

## Slide 14
  Parallel Priority
    Priority Encoder를 이용한 Parallel Priority : Fig. 11-14
      Interrupt Enable F/F (IEN) : set or cleared by the program
      Interrupt Status F/F (IST) : set or cleared by the encoder output
    Priority Encoder Truth Table : Tab. 11-2
  Interrupt Cycle
    At the end of each instruction cycle, CPU checks IEN and IST
    if both IEN and IST equal to “1”
    CPU goes to an Instruction Cycle
      Sequence of microoperation during Instruction Cycle
: Decrement stack point
: Push PC into stack
: Enable INTACK
: Transfer VAD to PC
: Disable further interrupts
Branch to ISR

## Slide 15
  Software Routines
    CPU main program KBD interrupt
    KBD service program DISK interrupt
KBD Int. Here
749
DISK Int. Here
255

## Slide 16
    Initial Operation of ISR
      1) Clear lower-level mask register bit
      2) Clear interrupt status bit IST
      3) Save contents of processor registers
      4) Set interrupt enable bit IEN
      5) Proceed with service routine
    Final Operation of ISR
      1) Clear interrupt enable bit IEN
      2) Restore contents of processor registers
      3) Clear the bit in the interrupt register belonging to the source that has been serviced
      4) Set lower-level priority bits in the mask register
      5) Restore return address into PC and set IEN
11-6 Direct Memory Access (DMA)
  DMA
    DMA controller takes over the buses to manage the transfer directly between the I/O device and memory (Bus Request/Grant)
Fig. 11-14

## Slide 17
  Transfer Modes
    1) Burst transfer : Block 단위 전송
    2) Cycle stealing transfer : Byte 단위 전송
  DMA Controller ( Intel 8237 DMAC ) : Fig. 11-17
    DMA Initialization Process
      1) Set Address register :
        memory address for read/write
      2) Set Word count register :
        the number of words to transfer
      3) Set transfer mode :
        read/write,
        burst/cycle stealing,
        I/O to I/O,
        I/O to Memory,
        Memory to Memory
        Memory search
        I/O search
      4) DMA transfer start : next section
      5) EOT (End of Transfer) :
        Interrupt 발생

## Slide 18
  DMA Transfer (I/O to Memory)
    1) I/O Device sends a DMA request
    2) DMAC activates the BR line
    3) CPU responds with BG line
    4) DMAC sends a DMA acknowledge
    to the I/O device
    5) I/O device puts a word in the data
    bus (for memory write)
    6) DMAC write a data to the address
    specified by Address register
    7) Decrement Word count register
    8) Word count register = 0 이면
    EOT interrupt 발생하여 CPU에 알림
    9) Word count register  0 이면
    DMAC checks the DMA request from
    I/O device

## Slide 19
11-7 Input-Output Processor (IOP)
  IOP : Fig. 11-19
    Communicate directly with all I/O devices
    Fetch and execute its own instruction
      IOP instructions are specifically designed to facilitate I/O transfer
      DMAC must be set up entirely by the CPU
    Designed to handle the details of I/O processing
  Command
    Instruction that are read form memory by an IOP
      Distinguish from instructions that are read by the CPU
      Commands are prepared by experienced programmers and are stored in memory
      Command word = IOP program

## Slide 20
  CPU - IOP Communication : Fig. 11-20
    Memory units acts as a message center : Information
      each processor leaves information for the other
Message Center
IOP Program
CPU Program

## Slide 21
  IBM 370 I/O Channel
    Channel = I/O Processor in IBM 370 computer
    Three types of channel
      1) Multiplexer channel : slow-medium speed device, operating with a number of I/O devices simultaneously
      2) Selector channel : high-speed device, one I/O operation at a time
      3) Block-Multiplexer channel : 1) + 2)
    I/O instruction format : Fig. 11-21(a)
      Operation code : 8 개
        Start I/O, Start I/O fast release (less CPU time),
        Test I/O, Clear I/O, Halt I/O, Halt device,
        Test channel, Store channel ID
    Channel Status Word : Fig. 11-21(b)
      Always stored in Address 64 in memory
      Key : Protection used to prevent unauthorized
      access
      Address : Last channel command word address
      used by channel
      Count : 0 (if successful transfer)

## Slide 22
    Channel Status Word : Fig. 11-21(c)
      Always stored in Address 72 in memory
      Command Code
        Write : transfer data from memory to I/O device
        Read : transfer data I/O device to memory
        Read backwards : read magnetic tape with tape moving backward
        Control : rewinding of tape, positioning a disk-access mechanism (HDD head control)
        Sense : inform the channel status word to the address 64 (Status Read)
        Transfer in channel : channel jump command (Channel change)
      Flags
        100000 : data chaining (same record)
        010000 : command chaining (same device)
        000000 : separate record,and End of I/O operation
    Example of a channel program : Tab. 11-3
3000
4000
6000
40
60
20
40
80
+
Tape
Memory
Same record
same device
Separate record
same device

## Slide 23
    Location of information in the IBM 370 : Fig. 11-22
     Address 72 에 I/O channel program의
    시작 Address (xxxx) 를 미리 설정
     CPU에 의해 Start I/O 명령 실행
     I/O channel program이 실행
     실행 결과를 Address 64에 저장




xxxx
xxxx
Fig. 11-21(b)
Fig. 11-21(a)
Fig. 11-21(c)

## Slide 24
  Intel 8089 IOP : Fig. 11-23
     CPU enables channel attention
     Select one of two channels of 8089
     8089 gets attention of the CPU by
    sending an interrupt request
  Location of Information : Fig. 11-24
    Channel Command Word (CCW) : message center
      Start command
      Suspend command
      Resume command
      Halt command




## Slide 25
11-8 Serial Communication
  Difference between I/O Processor and Data Communication Processor
    I/O Processor
      communicate with peripherals through a common I/O bus (data, address, control bus)
    Data Communication Processor
      communicate with each terminal through a single pair of wires
  Modem ( = Data Sets, Acoustic Couplers )
    Convert digital signals into audio tones to be transmitted over telephone lines
    Various modulation schemes are used (FM, AM, PCM)
  Block transfer
    An entire block of characters is transmitted in synchronous transmission
    Transmitter sends one more character (error check) after the entire block is sent
  Error Check
    LRC (Longitudinal Redundancy Check) : XOR
    CRC (Cyclic Redundancy Check) : Polynomial
  3 Transmission System
    Simplex : one direction only
    Half-duplex : both directions but only one direction at a time
    Full-duplex : both directions simultaneously
“Data Communication” 교과 참고

## Slide 26
  Data Link
    The communication lines, modems, and other equipment used in the transmission of information between two or more stations
  Data Link Protocol
    1) Character-Oriented Protocol
    2) Bit-Oriented Protocol
  Character-Oriented Protocol
    Message format for Character-Oriented Protocol : Fig. 11-25
      TEXT :
      BCC : Block Check Character (LRC or CRC)
    ASCII Communication Control Character : Tab. 11-4
      SYN (0010110) : Establishes synchronism
      SOH (0000001) : Start of Header (address or control information)
      STX (0000010) : Start of Text
      ETX (0000011) : End of Text
    Transmission Example : Tab. 11-5, 11-6

## Slide 27
  Data Transparency
    Character-Oriented Protocol에서 Binary Information을 전송하면, 이를 Control Character로 오인하여 문제가 발생
    따라서 Character-Oriented Protocol에서 Data Transparency를 해결하기 위해서 DLE (Data Link Escape) Character를 사용
  DLE
    Inserting a DLE character (bit pattern = 00010000) before each control character
      Exam) DLE ETX DLE SYN
    그러나 DLE character is inefficient and somewhat complicated to implement
    따라서 Bit-Oriented Protocol을 사용
  Bit-Oriented Protocol
    Transmit a serial bit stream (Frame) of any length without character boundaries
    Examples of bit-oriented protocol
      1) SDLC (Synchronous Data Link Control) : IBM
      2) HDLC (High-level Data Link Control) : ISO
      3) ADCCP (Advanced Data Communication Control Procedure) : ANSI
    Frame format for bit-oriented protocol : Fig. 11-26
      Flag : A frame starts and ends with 8-bit flag (01111110)

## Slide 28
    Zero Insertion
      Prevent a flag from occurring in the middle of a data frame
      Zero (0) is inserted by transmitting station after any succession of five continuous 1’s
        Example of zero insertion : 01111110 (data) 011111010
      Receiver always removes a 0 that follows a succession of five 1’s
    Control field format : Fig. 11-27
      1) Information Transfer : for ordinary data transmission
      2) Supervisory : for ready, busy condition check, ...
      3) Unnumbered : for initialization of link functions, reporting errors, ...
Security를 위하여 임의로 정의하여 사용함

## Slide 29
    Control Fields
      Ns : send frame count
      Nr : error free receive frame count
      P/F :
        P = 1 : primary station is finished and ready for the secondary station to respond
        P = 0 : each frame sent to the secondary station from the primary station
        F = 1 : secondary station sends the last frame
        F = 0 : secondary station responds with a number of frame (when primary station is finished)
      Code : type of command/response